## Slide 1: RSSI Gain Step Calibration in AD9361
Context: LO (Local Oscillator) & Gain Step Index
  Understanding RSSI behavior in SDR systems
  AGC interaction and calibration modeling

## Slide 2: Receiver Signal Chain
Antenna → LNA → Mixer (LO) → TIA → LPF → ADC → Digital
  RSSI measured after ADC
  Includes total analog + digital gain

## Slide 3: Gain Step Index (GSI)
Discrete gain control mechanism
  Each index = LNA + Mixer + TIA + Digital gain combination
  RSSI_raw = P_in + G_total
  P_in = RSSI_raw - G_total

## Slide 4: LO Dependency
LO sets RF center frequency
  Mixer conversion gain varies with LO frequency
  Gain flatness changes across bands
  G_total = f(GSI, LO_frequency)

## Slide 5: RSSI Computation
RSSI = 10 log10((1/N) * Σ(I² + Q²))
  Measured in dBFS internally
  Converted to dBm using gain tables

## Slide 6: Calibration Procedure
Inject known RF power (e.g., -60 dBm)
  Fix LO frequency
  Sweep Gain Step Index
  Store correction per (LO band, GSI)

## Slide 7: AGC Interaction
AGC dynamically changes GSI
  Without calibration: RSSI fluctuates
  Corrected: P_in = RSSI - GainTable[GSI]

## Slide 8: Non-Idealities
Gain ripple across frequency
  Step discontinuities
  Temperature drift
  LO leakage & DC offset

## Slide 9: Final Mathematical Model
P_in = 10log10((1/N)Σ(I²+Q²)) - G_analog(GSI,LO) - G_digital
  Calibration ensures accurate G_analog mapping
  Enables stable AGC & accurate power estimation